## Slide 1
New Jersey Fire Inspector Certification Program
New Jersey Uniform Fire Code
Fire Inspector Training Program
Based on the ICC IFC-2015 Edition with NJ adopted changes

## Slide 2: Fire Inspector Certification Program
New Jersey Uniform Fire Code Inspector Training Program
Module 2 Theory of Fire Code Enforcement
Education
Enforcement
Experience
Engineering
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
2
Opening Slide Module 2 Theory of Fire Code Enforcement

## Slide 3: Welcome
Instructor introduction
Before we get started
  Has everyone signed in?
  Anyone have any questions?
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
3
Self explanatory

## Slide 4: Theory of Fire Code Enforcement
In this module we will discuss…
How buildings are classified under the UCC-NJ,
Use Group classifications.
How UFC interfaces with UCC
How the different codes are applied,
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
4
Summary of objectives presented.

## Slide 5: Building Codes & Fire Codes
In NJ there are two different and distinct codes enforcement groups.
DFS
Div. of Fire Safety
Commissioner
Dept. of Community Affairs
DCS
Div. of Codes & Standards
UCC
UFC
UCC
UFC
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
5
In New Jersey the Department of Community Affairs control and regulates Construction code enforcement and fire prevention activities.
DCA Has two divisions served by a Commissioner
Division of Code & Standards (UCC)
Division of Fire Safety (UFC)

## Slide 6: Building Classifications
Prior to being constructed building go through a process termed- PLAN REVIEW.
The builder will work with an architect and develop plans which are submitted.
These plans are reviewed by the Planning Office, Zoning etc.
Once approval is granted the plans go to Construction under UCC
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
6
All buildings and structures need to be classified as to it actual use. The classification set the stage for how the buildings or structures will reviewed in accordance with code requirements.
Instructor may address how in their area, local or county planning is conducted.

## Slide 7: Building Classifications
The Construction office is responsible to review for code compliance.
One of the very first items this office will do is to classify the buildings use group
Each building use has very specific use parameters for construction and life safety requirements.
This classification is carried through the life of the building until it is either destroyed or a change of use occurs through UCC.
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
7
Once local or county planning boards approve a new building, the next step is the plan review process conducted by local, county or state officials to review, comment and request adjustments be made to comply with the code requirements.
NOTE: NJ UCC Overview describes how the UCC office,, Officials and plan review process is conducted in NJ.

## Slide 8: Code Application
As a fire inspector enforcing the UFC-NJ, One of our tasks is to maintain buildings and structures as they were approved and built under the UCC-NJ.
To do this task we need to know how the building or structure was approved and what systems were required.
An understanding of building classification is an essential element in the fire code enforcement process.
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
8
The UFC of NJ design is to effectively maintain how the building or structure was approved.

## Slide 9: Code Application
The NJ edition of the IFC adopted for the UFC is not to be used as the reference code for the application of UCC/IBC code requirements.
The regular Non-NJ (2015) edition of the IFC is the correct code to reference for the UCC/IBC.
These are two completely different codes.
Notes: Confusion can occur here for new students in addressing the different codes and when and where they apply or do not apply.

## Slide 10: Code Enforcement-NJ
Each DCA group specifies the codes used.
DFS
Div. of Fire Safety
Commissioner
Dept. of Community Affairs
DCS
Div. of Codes & Standards
UCC
UFC
2018 IBC w/ NJ Amendments
2014NEC
2018 IPC
2018 IFC
2015 IFC w/ NJ Amendments
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
10
Review slide

## Slide 11: Uniform Construction Code (UCC)
DCA
Commissioner
Bldg Inspector
Bldg Inspector
Bldg Inspector
Plumbing
Plumbing Inspector
Plumbing
Electrical Inspector
Fire Inspector
Electrical Inspector
Fire Inspector
Electrical
Fire Inspector
Construction Official
Building Subcode Official
Plumbing Subcode Official
Electrical Subcode Official
Fire Subcode Official
Notes: There are other subcodes .This chart is just a representation of the table of organization of typical UCC office in NJ. Some are smaller in staffed positoon other may be fully staffed.

## Slide 12: USE GROUP
“Use” or “Use Group” means the use to which a building, portion of a building, or premises, is put as follows. It shall also mean and include any place, whether constructed, manufactured or naturally occurring, whether fixed or mobile, that is used for human purpose or occupancy that would subject it to the provisions of this Code if it were a building or premises.
UCC Definition
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
12
Definition of USE GROUP taken from the UCC-NJ

## Slide 13: Use Groups
Use Group classification requirements and definitions are found in Chapter 3 of the IBC-NJ 2015.
Use Groups designations assigned pursuant to the UCC remain with the building or structure until changed by UCC or the building is destroyed
There is another list of Use Group designations found in the UFC that are utilized when we assess a structure for application of our Subchapter 4 retrofit requirements. These definitions do not match and do not change.
.
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
13

## Slide 14: Code Enforcement-NJ
The UFC-NJ employs two methods in the enforcement of the fire prevention code.
DFS
Div. of Fire Safety
UFC
Those buildings and structures built or constructed before January 1, 1977
Those buildings and structures built or constructed after January 1, 1977
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
14
Review Concepts of
Subchapter 3 General Maintenance Provisions
Subchapter 4 Retro Fit Code
Based off the Adoption of the UCC
January 1, 1977 date plays a important date and more will be discussed during Subchapter 4.

## Slide 15: Code Enforcement-NJ
Those Constructed under the UCC-NJ
Maintained as building and approved using the fire prevention code.
DFS
Div. of Fire Safety
UFC
Those buildings and structures built or constructed before January 1, 1977
Those buildings and structures built or constructed after January 1, 1977
Those Constructed prior to the UCC-NJ adoption.
Maintained as building and approved using the fire prevention code and Retro-code. (N.J.A.C. 5:70-4.1)
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
15

## Slide 16: Class assignment
List 10 Buildings and or structures and/or properties in your fire district or around your home or work.
List the name business/facility
What they do (Auto repair body shop, retail sales, business office)
(see previous homework assignment from student manual)
Lets review that homework now…………
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
16
Previous Class assignment.
Make sure all class attendee’s have completed homework assignment
Using flip charts, white board or other means, have each student write each of their 10 selected buildings.
Review th specific use of each with class.

## Slide 17: Use Groups
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
17
Self explanatory

## Slide 18: BUILDING CLASSIFICATION
A Assembly A-1, A-2, A-3, A-4, A-5
B Business
E Educational
F Factory F-1, F-2
H High Hazard H-1, H-2, H-3, H-4, H-5
I Institutional I-1, I-2, I-3, I-4
M Mercantile
R Residential R-1, R-2, R-3, R-4, R-5
S Storage S-1, S-2
U Utility
(Uniform Construction Code of N.J.)
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
18
Self explanatory Group slide the next series of slide will describe in better detail each of the USE GROUPS.

## Slide 19: ASSEMBLY
A-1 Use Group A-1 occupancy includes assembly uses, usually with fixed seating, intended for the production and viewing of the performing arts or motion pictures including, but not limited to:
  Motion picture theaters
  Symphony and concert halls
  Television and radio studios admitting an audience
  Theaters
A1 A2 A3 A4 A5
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
19

## Slide 20: Use Group A-1
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
20
Work directly from the building code book for this portion.

## Slide 21: Use Group A-1 - Theater
A1 A2 A3 A4 A5
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
21

## Slide 22: ASSEMBLY
A-2
Group A-2 occupancy includes uses intended for food and drink consumption including, but not limited to:
Banquet halls
Casinos (gaming areas)
Nightclubs
Restaurants, cafeterias and similar dining facilities (including associated commercial kitchens)
Taverns and Bars
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
22

## Slide 23: Use Group A-2 - Nightclub
A1 A2 A3 A4 A5
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
23

## Slide 24: Use Group A-2
USE GROUP A-2
A1 A2 A3 A4 A5
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
24
Self explanatory

## Slide 25: Use Group A-2 - Restaurant
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
25
Instructor notes:
Buildings built under ICC/IBC are classified as A-2. Previously they were considered an A-3 use

## Slide 26: ASSEMBLY
A-3 Group A-3 occupancy includes assembly uses intended for worship, recreation or amusement and other assembly uses not classified elsewhere in Group A including but not limited to:.
Amusement arcades
Art galleries,
Bowling Alleys
Community halls
Courtrooms
Dance Halls (not including food or drink consumption)
Exhibition halls
Funeral parlors
Museums
lecture halls
Libraries
buildings designed for other similar assembly purposes
A1 A2 A3 A4 A5
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
26

## Slide 27: Use Group A-3
USE GROUP A-4
A1 A2 A3 A4 A5
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
27
Self explanatory

## Slide 28: Use Group A-3
A1 A2 A3 A4 A5
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
28
Self explanatory

## Slide 29: ASSEMBLY
A-4 Group A-4 occupancy includes assembly uses intended for viewing of indoor sporting events and activities with spectator seating including but not limited to:
  Arenas
  Skating rinks
  Swimming pools
  Tennis courts
A1 A2 A3 A4 A5
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
29

## Slide 30: ASSEMBLY
A-5
Group A-5 occupancy includes assembly uses intended for participation in or viewing outdoor activities including but not limited to:
  Amusement park structures
  Bleachers
  Grandstands
  Stadiums
A1 A2 A3 A4 A5
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
30

## Slide 31: Use Group A-5 - Stadium
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
31
Self explanatory

## Slide 32: BUSINESS
B
Business Group B occupancy includes, among others, the use of a building or structure, or a portion thereof, for office, professional or service-type transactions, including storage of records and accounts. Business occupancies shall include, but not be limited to the following:
  Airport traffic control towers
  Ambulatory care facilities
  Animal hospitals, kennels and pounds
  Banks, business offices, architects and other similar facilities
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
32

## Slide 33: Use Group B - Office
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
33

## Slide 34: Use Group B
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
34
Self explanatory

## Slide 35: EDUCATION
E
Educational Group E includes among others, the use of a building or structure, or portion thereof, by six or more persons at any one time for educational purposes through the 12th grade.
Excludes religious schools accessory to place of worship
Includes day cares of five or more over 2 ½ years
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
35

## Slide 36: Use Group E - School
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
36

## Slide 37: FACTORY
F
Factory Industrial Group F occupancy includes, among others, the use of a building or structure, or a portion there of, for assembling, disassembling, fabricating, finishing, manufacturing packaging, repair or processing operations that are not classified as a Group H hazardous group or Group S storage occupancy
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
37

## Slide 38: Use Group F subgroups
    Group F-1: Factory and industrial uses which are not otherwise classified as low-hazard Use Group F-2, shall be classified as a moderate-hazard factory and industrial use, Use Group F-1
    Group F-2 Factory and industrial uses which involve the fabrication or manufacturing of non-combustible materials that, during finishing, packing or processing, do not contribute to a significant fire hazard, shall be classified as Use Group F—2. The following manufacturing processes are indicative of, and shall be classified as, Use Group F—2: beverages, nonalcoholic; brick and masonry; ceramic products; foundries; glass products; gypsum; ice; metal fabrication and assembly; and water pumping plants.

## Slide 39: Use Group F
Cheese Factory
Automated Factory
Auto Body
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
39

## Slide 40: Use Group F-1/H-2
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
40
Self explanatory

## Slide 41: HIGH HAZARD
High-hazard Group H occupancy includes, among others, the use of al building or structure, or portion thereof, that involves the manufacturing, processing, generation or storage of materials that constitute a physical or health hazard in quantities in excess of those allowed in control areas complying with section 414, based on the maximum allowable quantity limits for control areas…….Hazardous occupancies are classified in Groups H-1, H-2, H-3, H-4, and H-5….
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
41
Discuss Use groups H-1 thru H-5 individually

## Slide 42: Use Group H
Industrial Fermenter
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
42
Self explanatory

## Slide 43: Institutional Group I
Institutional Group I occupancy includes among others, the use of a building or structure or portion thereof, in which care or supervision is provided to persons where evacuation is slow or impractical, or in which persons are detained for penal or correctional purposes or in which the liberty of the occupants is restricted. Institutional occupancies shall be classified as:
I-1 includes Group homes, halfway houses, residential care facilities
I-2 includes hospitals, nursing homes, etc.
I-3 includes correctional centers, jails, prisons, etc.
I-4 includes adult day care, child day care
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
43

## Slide 44: Use Group I-1
USE GROUP I-1 Nursing Home
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
44
Self explanatory

## Slide 45: Use Group I-2
This Use Group shall include all buildings used for housing people suffering from physical limitations because of health or age, including, among others, day nurseries, hospitals, sanitariums, infirmaries, orphanages and homes for aged and infirm.
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
45

## Slide 46: Use Group I-3
“Use Group I—3”: This Use Group shall include all buildings designed for the detention of people under restraint, including, among others, jails, prisons, reformatories, insane asylums and similar uses.

## Slide 47: MERCANTILE
Mercantile Group M occupancy includes, among others, the use of a building or structure, or portion thereof, for display and sale of merchandise, and involves stocks of goods, wares or merchandise incidental to such purposes and accessible to the public. Mercantile occupancies shall include , but not be limited to the following:
  Department stores
  Markets
  Retail or wholesale stores and similar
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
47

## Slide 48: Use Group M - Store
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
48

## Slide 49: Use Group M
USE GROUP M Department Store
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
49
Self explanatory

## Slide 50: RESIDENTIAL
“Residential Group R includes, among others, the use of a building or structure, or a portion thereof, for sleeping purposes when not classified as an Institutional group I or when not regulated by the International Residential Code.
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
50

## Slide 51: RESIDENTIAL
“Use Group R—1”: This Use Group shall include all hotels, motels, and similar buildings arranged for shelter and sleeping accommodations and in which the occupants are primarily transient in nature.
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
51

## Slide 52: Use Group R-1
USE GROUPS R-1 Hotel
(Occupants are Primarily Transient)
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
52
Self explanatory

## Slide 53: RESIDENTIAL
“Use Group R—2”: This Use Group shall include all multiple family dwellings having more than two dwelling units and shall also include all dormitories, rooming houses, group rentals where the occupants are living independently of each other and similar buildings arranged for shelter and sleeping accommodations in which the occupants are primarily not transient in nature.
Apartments
Convents
Dormitory
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
53

## Slide 54: Use Group R-2
USE GROUPS R-2 Multi-family
(Occupants Primarily NOT Transient)
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
54
Self explanatory

## Slide 55: RESIDENTIAL
“Use Group R—3”: This Use Group shall include occupancies where the occupants are primarily permanent and not classified as Group R-1, R-2, R-4 or I including:
    Alcohol and drug treatment for five or fewer
    Boarding houses with five or fewer
    Group homes with five or fewer
    Rooming houses with five or fewer
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
55

## Slide 56: Use Group R-3
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
56
Self explanatory

## Slide 57: Use Group R-3 – Multiple Single Family
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
57

## Slide 58: RESIDENTIAL
Residential group R-4 occupancy shall include buildings, structures or portions therof for more than five but less than 16 persons, excluding staff, who reside on a 24-hour basis in a supervised residential environment, receive custodial care and are capable of slow evacuation.
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
58
CABO added for historical reference

## Slide 59: RESIDENTIAL
Residential Group R-5 occupancies shall include all detached one or two family dwellings not more than three stories in height and multiple single family townhouses not more than 3 stories in height designed and constructed in accordance with the International Residential Code.
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
59
CABO added for historical reference

## Slide 60: STORAGE
Storage Group S occupancy includes, among others, the use of a building or structure, or portion thereof, for storage that is not classified as a hazardous occupancy
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
60

## Slide 61: STORAGE S-1
Storage Group S-1 occupancy includes, among others, the use of a building or structure, or portion thereof, for storage that is not classified as S-2 including:
  Aerosol products Level 2 and 3
  Aircraft hangar(storage and repair)
  Belting, canvas
  Books and paper in rolls or packs
  Cardboard
  Clothing and similar products
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
61

## Slide 62: STORAGE S-2
Storage Group S-2 occupancies includes, among others, the use of a building or structure, or portion thereof, for storage of noncombustible materials. Group S-2 storage uses shall include, but not be limited to, storage of the following:
  Asbestos
  Beverages
  Cement in bags
  Dairy products
  Electrical coils, motors
  Food products………
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
62

## Slide 63: Use Group S-1 - Warehouse
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
63
Self explanatory

## Slide 64: Use Group S-1
USE GROUP S-1 Public Garage, Group 1
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
64
Self explanatory

## Slide 65: Summary
In this module will have discussed…
How buildings are classified under the UCC-NJ and UFC-NJ,
How the different codes are applied,
Defined Use Group classification with appropriate examples.
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
65
Summary of objectives presented.

## Slide 66: Review Questions
See student manual
  Module 2 - Module review questions

## Slide 67: Use Group/Life Hazard Use Homework
Refer to the pages in your student handout
Exercise #2
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
67
Two pages, one with short descriptions, one with a high school diagram.

## Slide 68: Next Lesson
Module 3
Code Administration
Date/time
Notes: Fire Code Enforcement I FIR -107
Entry Class Presentation
68
Review when the next class will be.

## Slide 69: Summary
In this Module we have discussed:
Course Parameters
Grading policy
Code History
State NJ Legislature
Uniform Construction Code
Basic Fire Science
Terms
Notes: Self explanatory

## Slide 70: Home work assignment
List on paper and bring to the next class
10 Buildings and or structures and or property in you or around your home, fire house, or work.
List the name
Address
What they do (Auto repair body shop, retail sales, business office)
(use the sheet provided in the student manual)

## Slide 71
END OF MODULE