## Slide 1: Fire Inspector Certification Program
New Jersey Uniform Fire Code Inspector training program
Module 8 General Precautions Against Fire
Part 1
Education
Enforcement
Experience
Engineering

## Slide 2: Welcome
Instructor introduction
Before we get started
  Has everyone signed in?
  Anyone have any questions?
Notes: Self explanatory

## Slide 3: General Fire Safety
In this module we will review…
State Fire Prevention Code
  Sub chapter 3 UFC NJAC 5:70-3.1
IFC 2015 NJ - Chapters 1 through Chapter 8

## Slide 4: IFC-2015 NJ Chapter 1 Administration
101.1 Purpose
101.2 Scope
101.3 Applicability
102.0 General Provisions
Notes: Utilize the PowerPoint slides as place holders. It is important that the instructor work directly from the code book during regulation lectures with the students following along in their own books.
Emphasize that not just fire safety hazards are covered, but in addition any “..condition hazardous to life, property or public welfare…”.
Ensure the students understand that in the case of process equipment the U.C.C. only worries about how the building features are effected, I.e., the means of egress, fire suppression, connection to utilities. The process equipment and operation itself is the responsibility of the fire code LEA.
Ensure the students understand that the general provisions in F-102.1 are only cited when a hazard is found that does not have a corresponding citation within the fire code or a directly referenced standard. If that occurs and a section of F-102.1 is cited, the citation must also include N.J.A.C. 5:70-1.3(b) and the section of the ‘Nationally Recognized’ standard that is being used to verify the hazard and provide for correction guidance.

## Slide 5: IFC-2015 NJ Chapter 1 Administration
102.1.1
  List of 10 dangerous conditions when no clear code language exists
  Should not be used as primary violation
103 Terms; Standards; Accepted Practice; Technical Assistance
  See 103.4
104 Maintenance
105 Service Utilities
Notes: Utilize the PowerPoint slides as place holders. It is important that the instructor work directly from the code book during regulation lectures with the students following along in their own books.
Emphasize that not just fire safety hazards are covered, but in addition any “..condition hazardous to life, property or public welfare…”.
Ensure the students understand that in the case of process equipment the U.C.C. only worries about how the building features are effected, I.e., the means of egress, fire suppression, connection to utilities. The process equipment and operation itself is the responsibility of the fire code LEA.
Ensure the students understand that the general provisions in F-102.1 are only cited when a hazard is found that does not have a corresponding citation within the fire code or a directly referenced standard. If that occurs and a section of F-102.1 is cited, the citation must also include N.J.A.C. 5:70-1.3(b) and the section of the ‘Nationally Recognized’ standard that is being used to verify the hazard and provide for correction guidance.

## Slide 6: Chapter 2 Definitions
201 General
  Scope
202 General Definitions
  Alphabetical listing
Notes: It is important to explain that when applying the code we use the definitions in this chapter, Subchapter 1, and the Uniform Fire Safety Act directly. If the word is not defined within these areas of law and code we then go to any of the definitions included in the U.C.C.
If you still did not find a definition you can use a related regulation or ordinance and then as a last resort you would go to s dictionary.
Point out that all words are listed in chapter 2 as a cross reference, but that some of the definitions are found in the related chapters.
Review some definitions that you as an instructor have had to refer to during your field experience under the U.F.C.

## Slide 7: Chapter 3 General Precautions against fire
301 General
302 Definitions
303 Asphalt Tar Kettles
304 Combustible Waste Materials
305 Ignition Sources
306 Motion Picture Projection Rooms
307 Open Burning & recreational fires
308 Open Flames
309 Powered Industrial Trucks & Equipment
310 Smoking
311 Vacant Properties
312 Vehicle Impact Protection
Notes: Transition slide.
General Precautions against fire
General
Definitions
Asphalt Tar Kettles
Combustible Waste Materials
Ignition Sources
Motion Picture Projection Rooms
Open Burning
Powered Industrial Trucks & Equipment
Smoking
Vacant Properties
Vehicle Impact Protection
Fueled Equipment
Indoor Displays
Misc Combustible Material Storage

## Slide 8: Chapter 3 General Precautions against fire
313 Fueled Equipment
314 Indoor Displays
315 Miscellaneous Combustible Material Storage
316 Hazards to Firefighters
317 Rooftop Gardens and Landscaped Roofs
318 Laundry Carts
319 Rooming and Boarding houses….
Notes: Transition slide.
General Precautions against fire
General
Definitions
Asphalt Tar Kettles
Combustible Waste Materials
Ignition Sources
Motion Picture Projection Rooms
Open Burning
Powered Industrial Trucks & Equipment
Smoking
Vacant Properties
Vehicle Impact Protection
Fueled Equipment
Indoor Displays
Misc Combustible Material Storage

## Slide 9: 303 Asphalt (tar) kettles
Notes: Review code requirements.

## Slide 10: 304 Combustible Waste Material
Type
Location
Capacity
Exceptions

## Slide 11: 305 Ignition Sources
Notes: Review code requirements.

## Slide 12: 305 Ignition Sources
Clearance
Proper disposal of hot ashes and Spontaneous ignition sources
Deliberate or negligent burning unlawful
Notes: Review code requirements.

## Slide 13: 306 Motion Picture Projection Rooms & Film
As per the UCC regulations at the time of construction or alteration.

## Slide 14: 307 Open burning
Notes: Review code requirements.

## Slide 15: 307 Open burning
Section covers both prohibited and allowable open burning
Special focus should be paid to Bonfires which has been a problem in New Jersey
These always require a Type 1 permit and inspection prior to approval
Notes: Review code requirements.

## Slide 16: 308 Open Flames

## Slide 17: 308 Open Flames
Section provides guidance for a wide variety of open flame applications:
  Use of Torches
  Open flame cooking
  Religious uses
  Flaming food preparation
  Sky lanterns
  Group A uses

## Slide 18: 309 Powered Industrial Trucks & Equipment

## Slide 19: 309 Powered Industrial Trucks & Equipment
Emphasis on hazards and control
  Battery Charging
  Fueling
  Repairs

## Slide 20: 310 Smoking

## Slide 21: 311 Vacant Premises
Notes: Review code requirements.
Blue button is linked to Building Evaluation of Vacant Buildings IAAI/FEMA to activate left click on button while in presentation mode.

## Slide 22: 311 Vacant Premises
This section covers all vacant spaces
Provides for firefighter safety initiatives through
  Placarding
  Safeguarding vacant spaces
  Eliminating ignition sources
  Removal of hazardous materials
Notes: Review code requirements.
Blue button is linked to Building Evaluation of Vacant Buildings IAAI/FEMA to activate left click on button while in presentation mode.

## Slide 23: 312 Vehicle Impact Protection

## Slide 24: 312 Vehicle Impact Protection
Technical specifications – 4 inch or 6 inch bollards listed
Fire Official responsible for the installation
This section referred to in other IFC chapters

## Slide 25: 313 Fueled Equipment
Lawn care , mopeds, motorcycles, cars portable equipment, cooking etc restricted interior use and storage.

## Slide 26: 314 Indoor Displays
Displays must not interfere with means of egress
Combustible Good restrictions
Vehicles on display (car shows)

## Slide 27: 315 Misc Combustible Material Storage
Approved areas
Clearances
Egress
Inside and Outside
Height limits
Locations

## Slide 28: 316 Hazards to Fire Fighters
  316.1 Trapdoors
  316.2 Shaft ways
  316.3 Pitfalls
  316.4 Obstruction on roofs
  316.5 Security device
  316.6 Structures and outdoor storage underneath high-voltage transmission lines

## Slide 29: 317 Roof Top Gardens and Landscaped Roofs
317 Roof Top Gardens and Landscaped Roofs
  317.1 General
  Sections 317.2 through 317.5
    317.2 Specifies Size limits and separations:
      15,625 Maximum Square footage
      125 foot maximum single edge
      6 foot separation from adjacent gardens and roofs
      Reference to UCC for design and construction

## Slide 30: 318 Laundry Carts
  318.1 Capacity 1 cubic yard or over
    Constructed of Non-Combustible material for use in Group B, E, F-1,I, M and R-1
    Exceptions:
      Area protected by an Approved Automatic sprinkler system
      Laundry carts in coin-operated laundries

## Slide 31: 319 Rooming and Boarding Houses and Residential Healthcare Facilities
319.1.1 Cooking limitations
319.1.2 Smoking restriction

## Slide 32: Chapter 4 Emergency Planning & Preparedness
401 General
403 Emergency Preparedness Requirements
404 Fire Safety & Evacuation and Lockdown
Plans
405 Emergency Evacuation Drills
406 Employee Training & Response
Procedures

## Slide 33: Chapter 4 Emergency Planning & Preparedness
407 Hazard Communication
408.15 Hospitality rooms

## Slide 34: Chapter 4 Emergency Planning & Preparedness
Use Groups A, E, H-5 I-1, I-2,I-3
R-1
R-2
R-4
Covered mall
Approval, revisions Tenant ID Maintenance.

## Slide 35: 403 Emergency Preparedness Requirements
Fire Watch
Public Safety Plans
Use specific –previous slide
IAP
Notes: Review code requirements.

## Slide 36: 404 Fire Safety Evacuation plans
Who is required
Contents
Evacuation Plan
Fire Safety Plan
Evacuation Drills
Employee Training & Response Procedure
Hazard Communication

## Slide 37: 405 Emergency Evacuation Drills
Part of the inspectors document review
Notes: Review code requirements.

## Slide 38: Section 406
Employee Training & Response Procedures

## Slide 39: Section 407
Hazard Communication

## Slide 40: 408.15 Hospitality Rooms
Requirements similar to 403.15 Group overnight stays
Notes: Review code requirements.

## Slide 41: Rooming & boarding houses
Notes: Review code requirements.

## Slide 42: Use Group I-1
Notes: Review code requirements.

## Slide 43: Use Group I-2
Notes: Review code requirements.

## Slide 44: Use Group I-3
Notes: Review code requirements.

## Slide 45: Summary
In this module Part 1 we reviewed…
State Fire Prevention Code Sub-Chapters 3-
  IFC Chapters 1 through 4
Notes: Self explanatory.

## Slide 46: Review Question
See student manual for Review questions
  Module 8 General hazards

## Slide 47: Next Lesson
Module 8
Part 2
Notes: Review when the next class will be.

## Slide 48: Homework Assignments
For next module as stated in the syllabus
Notes: Remind the students about the reading assignment in the syllabus.

## Slide 49
End of Module